## Slide 1: Simulated Measurements Overview
Goal: Generate IMU data for EKF testing
Process:
- Use real flight data
- Generate truth IMU
- Inject sensor errors

## Slide 2: Data Source
OpenSky flight trajectories
Sampled at 0.1 Hz
Includes:
- Time
- Lat/Lon
- Speed
- Heading
- Vertical rate
- Altitude

## Slide 3: Preprocessing
Filtered non-flight data
Removed incomplete flights
Kept continuous trajectories only

## Slide 4: Interpolation
Upsampled to 10 Hz
Used PCHIP interpolation
Reason:
- Avoid oscillations
- Preserve smooth trajectory

## Slide 5: NED Conversion
Converted velocity to NED frame
VN = Vh cos(psi)
VE = Vh sin(psi)
VD = -V_vertical

## Slide 6: Acceleration (Truth)
Computed via numerical gradient
an = dVn/dt
Represents true acceleration in NED frame

## Slide 7: Euler Angles
Yaw = heading
Pitch = flight path angle
Roll = coordinated turn assumption
Rates computed via gradient

## Slide 8: Gyroscope Measurements
Body rates [p q r] computed from Euler angle rates
Using standard transformation matrix

## Slide 9: Specific Force
f_nav = a_nav - g
Converted to body frame using 3-2-1 DCM

## Slide 10: Validation
Integrated acceleration
Compared velocity to original trajectory
Confirmed consistency

## Slide 11: Error Injection
Added IMU errors:
- Bias
- Cross-axis sensitivity
- Noise
No temperature modeling

## Slide 12: Final Output
Body-frame specific force
Body-frame angular rates
Includes injected errors
All at 10 Hz